## Slide 1: Galden® - PFPEs Comparison with other Heat Transfer fluids
2021
2023

## Slide 2: What are PFPEs
PerFluoroPolyEthers (PFPEs) are clear and colorless fluoropolymer, liquid in a wide range of temperatures and based on a proprietary and unique technology composed entirely of:
C-C and C-O
bonds shielded by a cloud of F
C-F
the strongest bond in organic chemistry
  Carbon
  Oxygen
  Fluorine
CF3O-[(CF2CF2O)m-(CF2O)n]-CF3
CF3O-[(CF2 CFO)m-(CF2O)n]-CF3
CF3
Linear
Branched

## Slide 3: PFPEs Chemistry Effect
    Features due to the presence of Fluorine
      Excellent thermal and oxidative stability
      Excellent chemical stability
      Dielectric properties
      Non flammable
      Low surface energy
Features due to the presence of Oxygen
  Imparts flexibility to the polymer chain
  Liquid in a very large temperature range
  Excellent flow behavior at low temperature
  Higher viscosity index (VI) for linear PFPE (higher O/C ratio)

## Slide 4: Features and benefits
Features | Benefits
Low evaporation rate | Less consumption and lower cost of ownership
Safety | Non-flammable (no flash point), low toxicity
Excellent compatibility | Variety of plastics, metals and elastomers
Wide temperature range | Good viscosity at low temperatures
Electrical Properties | High dielectric strength, high resistivity
Low miscibility with water and solvent | Easy to recover in case of leakage and no residue

## Slide 5: Safety First - Flash and Fire Point
Compared to other widely used fluids and oils Galden® PFPEs have no incendiary risk
PFPE have no FLASH, no FIRE and no Autoignition point
Flash Point: Temperature above which a fluid emits vapors that can be ignited
Fire Point: Temperature above which a fluid emits vapors that can sustain a flame
Autoignition Point: Temperature above which a fluid combust without external ignition sources
Approved under FM 6930 Standard
Fire Control System not Required

## Slide 6: Galden® PFPE vs Polyester Comparison
Property | Galden® EV110 - PFPE | Polyester Oils | Synthetic hydrogenated Oils (alkyl, alkylbenzene, etc.) | Silicone Oils
Flammability | No Flash Point Totally non-flammable Fire extinguishing properties FM6930 Approved | Flash Point present (example: 170°C) Flammable | Flash Point present (example: 142°C) Flammable The less viscous/lower boiling point the more flammable | Flash point present above 250°C Flammable
Stability | No decomposition up to 290°C No degradation over time | Oxidation possible if not inhibited by additives (additives deplete over time) | Oxidation and even carbonization possible if not inhibited by additives (additives may deplete over time) | Tend to change viscosity over time due to oxidation + cross-linking → “gelation”
Compatibility | Excellent Compatibility with rubbers and thermoplastics (excluding only fully fluorinated elastomers) | Fair compatibility with thermoplastics Leach out risk with elastomers and their additives | Fair compatibility with thermoplastics Leach out risk with elastomers and their additives | Good Compatibility with rubbers and thermoplastics Excluding silicones
Water miscibility | <10 ppm | More than 1000 ppm can be absorbed (as reported in producer’s brochure) | Typically tens to hundreds of ppm (50 to 200 ppm) | Typically hundreds of ppm (100 to 900 ppm)

## Slide 7: Galden® PFPE vs Polyester Comparison
Property | Galden® EV110 - PFPE | Polyester Oils | Synthetic hydrogenated Oils (alkyl, alkylbenzene, etc.) | Silicone Oils
Recyclability/ Reuse | Infinitely recyclable/reusable if kept below its degradation point | Degrades over time and will need to be changed and disposed Recyclability is questionable | Degrades over time and will need to be changed and disposed Recyclability is questionable | Degrades over time and will need to be changed and disposed Recyclability is questionable
Electrical Resistance | Extremely High Very stable over time | Very High but: could be influenced by water absorption | Very High but: carbonization can reduce resistivity | Very High but: could be influenced by water absorption
Breakdown Voltage | 40 kV at 2.54 mm | Since dielectric strength depends on humidity rather than on the product insulation quality, the breakdown voltage can vary significantly | Since dielectric strength depends on humidity rather than on the product insulation quality, the breakdown voltage can vary significantly | Since dielectric strength depends on humidity rather than on the product insulation quality, the breakdown voltage can vary significantly
Safety in case of accident/spillage | No odor Can be easily recovered and any minor residues evaporate on their own Non-toxic | Mild odor Soluble in other oils/greases making recovery more challenging Typically non-toxic | Mild to strong odor Soluble in other oils/greases making recovery more challenging Can be toxic to aquatic environment | Mild odor Stains and easily spreads across and permeates surfaces → difficult to recover Typically non-toxic

## Slide 8: Material Compatibility (@ 25 °C)
✔ Good 一 Fair ✗ Poor |  | Synthetics Hydrocarbons | Glycols | Esters | Silicones | Galden® Fluorinated Ethers - PFPE
Plastics | Acetals | ✔ | ✔ | ✔ | ✔ | ✔
 | Phenolics | ✔ | ✔ | ✔ | ✔ | ✔
 | Terephthalates | ✔ | ✔ | ✔ | ✔ | ✔
 | Polycarbonates | ✔ | ✗ | ✗ | ✔ | ✔
 | A-b-s Resins | ✔ | ✗ | ✗ | ✔ | ✔
 | Polyphenylene Oxides | ✔ | ✗ | ✗ | ✔ | ✔
 | Polysulfones | ✔ | ✗ | ✗ | ✔ | ✔
 | Nylon (Polyamide) | ✔ | ✔ | ✔ | ✔ | ✔
 | Polypropylene | ✔ | 一 | 一 | ✔ | ✔
 | Polyethylene | 一 | 一 | 一 | ✔ | ✔
Elastomers | Natural Rubber | ✗ | ✗ | ✗ | ✔ | ✔
 | Buna S | ✗ | ✗ | ✗ | ✔ | ✔
 | Butyl | ✗ | ✗ | ✗ | ✔ | ✔
 | Ethylene Propylene | ✗ | 一 | 一 | ✔ | ✔
 | Nitrile (Buna N) | ✔ | 一 | 一 | ✔ | ✔
 | Neoprene | ✔ | ✗ | ✗ | ✔ | ✔
 | Silicone | 一 | 一 | 一 | ✗ | ✔
 | Fluoroelastomers | ✔ | ✔ | ✔ | ✔ | ✔

## Slide 9: Thank you.
Follow us on
Please consider that all data in this presentation is not to be considered subject to specification, it is provided in good faith, for reference purposes only and it does not relieve the customer from using his best judgment and knowledge while selecting, using and processing our materials.

## Slide 10: “There are no limits to what science can explore.” Ernest Solvay